## Slide 1: Teledyne API – San Diego Facility

## Slide 2
Teledyne-API is a leading supplier of the following instrumentation products and services:
Ambient air quality gas analyzers
Source level emissions gas analyzers
Zero-air Generators
Dynamic Dilution Calibrators
Particulate Monitors
Technical support services
  Service support
  Repair
  Training

## Slide 3
Ambient air quality gas analyzers:
T Series & N Series gas analyzers
Gases measured:
  SO2, H2S, TRS, TS
  NO, NO2, NOx, NOy, NH3, “True NO2”, “Direct NO2”
  CO, CO2
  O2, O3
Measurement technologies:
  UV Fluorescence
  Chemiluminescent w/ Moly or Photolytic Converter; Cavity Attenuated Phase Shift (CAPS)
  IR Gas Filter Correlation
  UV Absorption
  Paramagnetic
Most analyzers available in ambient, source and trace level versions
All ambient analyzer models US EPA FEM or FRM approved
T-API provides many analyzers to federal, state and local regulatory agencies, including: USEPA, CARB, SCAQMD, SDAPCD, etc.
NumaView software

## Slide 4
Source level emissions gas analyzers:
T Series and N Series gas analyzers
Gases measured:
  SO2, TRS
  NO, NO2, NOx
  CO, CO2,
  O2
Measurement technologies:
  UV Fluorescence
  Chemiluminescent w/ Moly or SS converter
  Gas Filter Correlation IR
  Paramagnetic
Most analyzers available in mid and high level versions, with dual ranges
T-API provides analyzers to many CEMS integrators for compliance monitoring
NumaView software

## Slide 5: N Series Gas Instruments
September, 2022

## Slide 6: N Series Highlights
Smart Internal Hardware Modules
  — Easy field replacement with pre-calibrated and tested modules
CAN Bus Communications Architecture
  — Simplified, common cabling for increased reliability
24VDC Internal Power
  — Lower power consumption and unified power requirement
Split Fold-down Rear Panel
  — Access to internal pneumatic connections
NumaViewTM Software Interface
  — Familiar, mature, and customizable with real-time graphing, diagnostic alerts, and preventative maintenance capabilities
Flow System Module with Pump Duty Cycle Control*
  — Reduces pump duty cycle for increased lifetime
* PDCC is on internal pumps only for certain models

## Slide 7: N Series Front Panel
Standard 19” rack mountable chassis
Optional ears, handles, and/or slides
Capacitive, color touch-screen display
2 front-panel USB ports
Soft power switch

## Slide 8: N Series Rear Panel
Split fold-down rear panel
Robust pneumatic bulkhead fittings
Ethernet and serial communications with Modbus protocol
Analog output and Digital expansion cards (optional)

## Slide 9: Traditional Gas Instrument Wiring Architecture
Requires host controller (motherboard)
Multiple power supplies
Relay board to transmit power
Analog signals transmitted separately
Many, many electrical connections and variable cable styles

## Slide 10: N Series Wiring Architecture
Single, universal power supply
Power and data provided in a single cable set
All CAN Bus cables and connectors are common
Simplified cabling and connections = improved reliability!!

## Slide 11: Common Smart Modules
Mainboard Module
  — Serves as the “carrier board” for the CPU
  — Provides the core set of user-accessible I/O, including Ethernet and Serial ports
  — DC power distribution and CAN bus hub
  — Provides all power management including soft power switch
Communication Modules
  — Digital I/O expansion
    Status out, control in, alarm relays
  — Analog outputs
    3 x current (4-20 mA)
    4 x voltage (5 or 10V)

## Slide 12: N Series CEM Instrument Models

## Slide 13: Internal Layout (N200M)
Common electronics with a single 24VDC power supply
Sensor smart module
Split fold-down rear panel
Optional integrated paramagnetic O2 sensor
Ozone generator smart module

## Slide 14: Internal Layout (N300)
Flow system smart module with Pulse-width modulated (PWM) control
Internal Zero/Span Valve Assy*
Long-life or 47mm sample filter holders*
*options available on ambient models

## Slide 15: NumaViewTM Software Interface
  Customizable, content rich, and intuitive user interface
User-definable meter variables

## Slide 16: Intuitive User Interface
  Real-time graphical representation of concentration and stability

## Slide 17: Intuitive User Interface
  Fully configurable dashboard

## Slide 18: Intuitive User Interface
  Real-time graphical representation of test functions

## Slide 19: Intuitive User Interface
  Simultaneous display of all active alerts with time stamp and cause

## Slide 20: Intuitive User Interface
  Custom events and warnings

## Slide 21: Intuitive User Interface
  Simple Calibrations

## Slide 22: Data Acquisition and Logging
  Triggers for data logging, including periodic and conditional

## Slide 23: Data Acquisition and Logging
  Customizable datasets that can be viewed on the GUI

## Slide 24: Full USB Support
  Data Upload and Download

## Slide 25: Analog Outputs
  Easily map any data ‘tags’ to any analog output

## Slide 26: Teledyne API N Series Gas Analyzers
Designed for today, prepared for tomorrow

## Slide 27: T Series… Stack Instruments
T100 SO2 Analyzer
T100H High-Level SO2 Analyzer
T101 H2S Analyzer
T102 TRS Analyzer
T108 Total Sulfur Analyzer
T200 Low-Level NOx Analyzer
T200M Mid-Level NOx Analyzer
T200H High-Level NOx Analyzer
T300U Ultra Low-Level CO Analyzer
T300 Low-Level CO Analyzer
T300M Mid-Level CO Analyzer
T360 CO2 Analyzer
T360M Mid-Level CO2 Analyzer
T802 Oxygen Analyzer*
Optional Paramagnetic O2 Sensor
*Optional NDIR CO2 Sensor

## Slide 28: T Series CO Instrument Models
T300U
  Range: 0 -100 ppm
  LDL: < 20 ppb
T300
  Range: 0 – 1,000 ppm
  LDL: < 0.04 ppm
T300M
  Range: 0 – 5,000 ppm
  LDL: 0.2 ppm

## Slide 29: T Series NOx Instrument Models
T200
  Range: 0 – 20 ppm
  LDL: 0.04 ppb
T200M
  Range: 0 – 200 ppm
  LDL: 40 ppb
T200H
  Range: 0 – 5,000 ppm
  LDL: 40 ppb

## Slide 30: Choosing a NOx Converter
For ambient applications, the choice is simple: Use a molybdenum catalytic converter, heated to 315oC. This will convert >98% of the NO2.
MOLY
ANALYSIS
PUMP
SAMPLE

## Slide 31: Choosing a NOx Converter
The choice, when sampling stacks, requires a little thought. First you need to determine the level of NO2 that you expect the analyzer to see. Typically, the hotter the combustion process, the more NO2 will be produced.
T200M

## Slide 32: Choosing a NOx Converter
Probe
Heated Sample Line
Sample Conditioner
Sample Pump
RULE #1: If the expected NO2 concentration in your straight-extractive system is less than 5 ppm, and the total NOx is less than 10 ppm, use a Model T200 with an internal molybdenum converter. If it is greater than 5 ppm and less than 100 ppm, use the Model T200M or T200H with a moly.
T200

## Slide 33: Choosing a NOx Converter
Probe
Heated Sample Line
Sample Conditioner
Sample Pump
T200H
RULE #2: If the expected NO2 concentration in your straight-extractive system is greater than 25 ppm, and you can tolerate conversion efficiencies as low as 85%, use the Model T200H with an internal “Mini-Hicon”, a stainless steel, high-temperature converter.

## Slide 34: Choosing a NOx Converter
In summary, for straight-extractive systems:
[NO2] < 5 ppm & [NOx] < 20 ppm & Efficiency >98%
Analyzer = Model T200, Converter = Moly
[NO2 ] > 5 ppm and < 100 ppm & Efficiency >98%
Analyzer = Model T200H or T200M, Converter = Moly
[NO2] > 25 ppm & 85% < Efficiency <100%
Analyzer = Model T200H, Converter = Mini Hicon

## Slide 35: Final Test Validation Sheet

## Slide 36: Health Status Report
New Health Status Report for a quick snapshot of analyzer operational ‘health’

## Slide 37: New Webstore
Purchase spare parts, maintenance kits and training with a credit card
store.teledyne-api.com

## Slide 38: TAPI Tech Support
No charge for the life of the instrument
Email: API-techsupport@teledyne.com
Phone: 1-858-657-9800
Secure Support:
  http://eservices.teledyne-api.com/services/Users/user_login.asp
RMA or field service request
  http://www.teledyne-api.com/service-support/rma

## Slide 39: Questions?