## Slide 1: Cedar Software – What’s New – What’s Coming
Kevin Batchelder
Lead Software Developer
September 13, 2022

## Slide 2: breez75
Few changes – mostly stable
Minor improvements for monitored bypass stacks

## Slide 3: breez75 / ECMPS 2.0
EPA effort to redesign ECMPS
  Convert Client Tool to browser-based application
  Reduce calls to CAMD for technical support
Now slated for Q1 2024
Updates at ecmps.blogspot.com

## Slide 4: Redundant Cedar Servers
Primary and secondary servers
Redundant database on each server
Both servers run 24/7
Data synchronization, typically within 10 minutes
Secondary server takes over when primary is unavailable
Cedar Data Monitor automatically switches to secondary
Automatically switches back when primary is available again
Cedar 7

## Slide 5: Redundant Cedar Servers
Ongoing performance enhancements
Reduction of unnecessary alarms
When Cedar Data Monitor starts up, can now connect to secondary server if primary server unavailable
Cedar 7

## Slide 6: New Jersey EEMPR
Regulatory changes effective 2022
3-hour rolling averages -- New method for determining exceedance duration
Cedar 7.37

## Slide 7: Alberta
Regulatory changes for 1-1-2022
New codes for electronic reporting
Alberta data substitution
Cedar 7.37

## Slide 8: CGA/Linearity Alarms
New checks for CGAs (missing or failed)
Alarm for 4 quarters with no linearity check
Warning alarm for 168+ op hours but no linearity check
Warning alarm for op time but no CGA
New support for custom alarms based on CGA/linearity status
Cedar 7.38

## Slide 9: Other Changes
Improve performance of exceedance/downtime rebuild for startup/shutdown events
Reports – add support for tab-delimited export
Spanish language support
  CeDAR applications
  Dual-language configuration
Cedar 7.39

## Slide 10: Cylinder Manager
Demo

## Slide 11: Cylinder Manager
List of available cylinders
List of in-service cylinders
Gas profiles show all current cylinder data in CEMS PLCs

## Slide 12: Cylinder Manager
Drag-and-drop to change cylinder
Changes propagate everywhere that uses the same cylinder
Changes from CEMS HMI panel also propagate

## Slide 13: CiSCO Software
Questions?